## Slide 1
SINGAPORE DEFENCE TECH HACKATHON
Team WISL
A mission-memory layer for cheap drone fleets
01 / 17

## Slide 2
01 — THE CLAIM
The honest claim, stated precisely.
Robotic failures are valuable data — but only if you can get to it. Today it's trapped in vendor-specific formats, scattered across silos, unreadable without an engineer in the loop. WISL turns transient mission failures into a permanent, queryable institutional record.
WHAT WISL IS NOT
• Real-time tactical advantage
• Site defense or target engagement
• A swarm-rescue mid-engagement
WHAT WISL IS
• A permanent record of every mission failure
• Queryable across the whole fleet, one schema
• A record no vendor can take away from you
02 / 17

## Slide 3
02 — WHERE IT PAYS OFF
One quadrant. We're deliberately not chasing the other three.
CHEAP · ONE-OFF
Expected losses
CHEAP · SYSTEMATIC
WISL's target
DJI · PX4/Auterion · ArduPilot — batch defect, firmware bug, jamming vulnerability — caught once, fixed across hundreds of units.
EXPENSIVE · ONE-OFF
Diagnosable the old way
EXPENSIVE · SYSTEMATIC
Rare in practice
ONE-OFF FAILURE
SYSTEMATIC FAILURE
WHY THIS QUADRANT
Losing one $2,000 DJI unit to a random crash is an expected cost of flying at that price. The value shows up when the same failure repeats across a fleet large enough that it will happen again — unless someone writes it down once.
03 / 17

## Slide 4
03 — THE MECHANISM
The actual pipeline, live today.
EDGE
Hash & upload
→
QUEUE
Redis
→
WORKER
Parse & normalize
→
SCHEMA
Canonical L2 JSON
→
DETECT
Physics thresholds
SIGNAL | THRESHOLD | WHY
Battery | ≤20% / ≤10% | Low / failsafe band
Altitude step | ≥25 m or 20 m/s | Faster than any real climb
Ground speed | 120 m/s air · 15 m/s ground | Above brand cruise ceiling → GPS jump
Attitude | ≥40° / ≥70° | Past level flight → tumble band
Telemetry gap | ≥15 s | Dropout, not jitter
04 / 17

## Slide 5
04 WHAT WE ACTUALLY RAN
Counts are files the parsers accept. Demo uses a subset.
2
DJI CSV DEMO
alpha + bravo controller fixtures
Recurring operator_warning. min_flights=2.
3
PX4 ULOG
recorded .ulg on disk
pytest parse_px4_ulg_to_l1 on the sample ULog.
2+1
ARDUPILOT
DataFlash .bin + MAVLink .tlog
pytest: crash bin, log171.bin, flight.tlog.
6471
VISDRONE DET
6471 train / 548 val stills
camera_frame + frame_census on recorded_at.
05 / 17

## Slide 6
05 THE DEMO
Upload a raw log. GET /v1/flights/{id}/path drives Cesium.
CESIUMJS · WGS84 TERRAIN · OSM IMAGERY
Two DJI CSVs. Both emit operator_warning.
GPS signal weak on alpha and bravo
GET /v1/incidents/patterns at min_flights=2
PATH
Trajectory from /v1/flights/{id}/path on the recorded clock.
SIGNATURE RECURS AT 2 FLIGHTS
patterns: flight count, incident count, first/last seen.
MITIGATION BULLETIN
POST /v1/mitigation-bulletins writes an operator briefing document.
06 / 17

## Slide 7
06 FUTURE EXPANSION
Fine-tune is still a dry-run. Landing-zone occupancy is next.
OPEN
VisDrone DET fine-tune
finetune_eval.json is dry_run true. mAP50 is null. YOLOv8n stays COCO-pretrained. No edge weights.
NEXT
Landing-zone occupancy
Combine frame_census with altitude from L2. Globe-projected boxes stay out until camera intrinsics exist on the log.
07 / 17

## Slide 8
07 — CLOSE
Thank you.
WISL doesn't need to win the engagement to be valuable — making the next mission better informed is enough.
WISL
Questions welcome — appendix follows
08 / 17

## Slide 9
APPENDIX
Backup.
Architecture, detection, stack, vision corpus. A3-A5 stay as offline looks, not ingest proof.
A1 System architecture
A2 Detection logic, in full
A3 Dataset — operations log
A4 Dataset — live telemetry
A5 Dataset — DJI warning corpus
A6 Dataset — vision corpus
A7 Stack
A8 Anticipated questions
09 / 17

## Slide 10
A1 — SYSTEM ARCHITECTURE
Every hop from upload to bulletin.
ENDPOINT | PURPOSE
POST /v1/logs/upload | SHA-256-hashed multipart upload, idempotent on the hash
GET /v1/logs/{id}/status | received → parsing → normalizing → detecting → ready
GET /v1/flights/{id}/path | Trajectory for the replay client
GET /v1/flights/{id}/incidents | Detected incidents for one flight
GET /v1/incidents/patterns | Signatures recurring across ≥2 flights
GET /v1/mitigation-bulletins | Generated bulletin per recurring signature
POST visuals / GET census | camera_frame store; frame_census on recorded_at for HUD
Canonical schema: position · attitude · battery · sensors · metadata
Brand match: ordered substring scan, DJI → PX4 → ArduPilot → legacy, first hit wins
10 / 17

## Slide 11
A2 — DETECTION LOGIC, IN FULL
Physics detectors on L2 JSON. Demo signature is operator_warning.
RULE | FIRES AT | SEVERITY
battery_low / battery_critical | ≤20% / ≤10% | warning / critical
battery_plunge | ≥15 pts drop in 60 s | critical
altitude_spike | ≥25 m or ≥20 m/s | warning, critical at 2×
gps_jump | ≥120 m/s air · ≥15 m/s ground | critical
attitude_shock | ≥40° / ≥70° roll or pitch | warning / critical
telemetry_gap | ≥15 s between samples | warning
Same-type incidents within 5 s merge. Ground-speed ceiling is the only brand-dependent constant, via identify_brand(). Also: operator_warning from APP.warning; UXO flags mission_incomplete, last_known_position, operator_marked_debris.
11 / 17

## Slide 12
A3 — DATASET: OPERATIONS LOG
554 real mission logs, per-flight summaries.
547
COMPLETED FLIGHTS
0 false positives on the battery threshold.
5
LABELED REAL FAILURES
4 correctly left unflagged — overweight payload, empty tank, not battery events.
78%
ONE REAL GAP FOUND
A flight logged “battery failure” landed with 78% remaining — state-of-charge alone can't catch it.
2
MALFORMED ROWS
Unquoted commas shifted columns — found, not silently ingested.
12 / 17

## Slide 13
A4 — DATASET: LIVE TELEMETRY
785 real GPS + battery samples, two flights.
2
CLEAN NOMINAL FLIGHTS
Real lat/lon/altitude/battery% — no synthesis needed.
0
INCIDENTS RAISED
Correct true-negative — max climb 5 m/s, max speed 15.8 m/s, both inside limits.
gimbal ≠ airframe
CAVEAT FOUND
Camera gimbal angle isn't aircraft attitude — mapped yaw only, left roll/pitch unset.
4.58, 4.58
BROKEN FIELD FLAGGED
homeLatitude/homeLongitude is a static placeholder in every sample.
13 / 17

## Slide 14
A5 — DATASET: DJI WARNING CORPUS
1,853 real in-flight messages, 12 DJI models.
683
MATCHED OUR KEYWORDS
37% of real messages hit the existing warning-keyword list.
12
DJI MODELS COVERED
Inspire, Mavic, Phantom, Matrice, Spark, S1000+.
Code: 30183
IMPROVEMENT FOUND
Real warnings carry stable numeric codes — more robust than keyword matching, not yet wired in.
14 / 17

## Slide 15
A6 DATASET: VISION CORPUS
VisDrone2019-DET stills. Fine-tune set. Not VID. Not telemetry.
6471
TRAIN STILLS
VisDrone2019-DET train, 1:1 txt boxes.
548
VAL
mAP gate. finetune_eval.json is still dry_run.
1610
TEST-DEV
Hold-out after val. Drop class 0 ignored regions.
camera_frame
WHERE IT LANDS
frame_census on recorded_at. HUD cars N · people M.
15 / 17

## Slide 16
A7 — STACK
No step is cloud-dependent except one.
Ingest / API | FastAPI, Redis queue, background worker
Physics detect | stdlib thresholds on L2 JSON
Narrative layer | Self-hosted LLM, schema-validated output, auto-retry on failure
Replay | CesiumJS, WGS84 terrain, OpenStreetMap imagery
Storage / vision | SQLite + visuals_dir. Optional YOLOv8n sidecar; frame_census HUD.
16 / 17

## Slide 17
A8 — ANTICIPATED QUESTIONS
Questions we expect, answered in advance.
Why thresholds for aircraft health?
Explainable, identical across brands, grounded in published failsafe bands. ML is reserved for ground-object census.
Why pivot away from named tactical platforms?
Cheap, large fleets are where a systematic failure actually repeats often enough for a shared record to pay for itself.
What about a raw PX4 ULog or ArduPilot DataFlash file?
Parsers and tests exist on real files in raw_telemetry-datasets/ (3 ULog, 2 DataFlash, 1 tlog).
Is any part of this cloud-dependent?
Only the narrative-summary layer, and that's a self-hosted model, never a cloud API.
How does the vision layer fit in?
HUD and census API are wired. VisDrone DET fine-tune has not been run. No onboard detector. No globe-projected boxes.
17 / 17